## Slide 1: AERO: Adaptive Erase Operation for Improving Lifetime and Performance of Modern NAND Flash-Based SSDs
Sungjun Cho1, Beomjun Kim2, Hyunuk Cho1, Gyeongseob Seo2,
Onur Mutlu3, Myungsuk Kim2, Jisung Park1
1
2
3
ASPLOS 2024
Session 9B: SSDs

## Slide 2: Executive Summary
Problem
Long and fixed latency of erase operation in modern SSDs degrade lifetime and I/O performance
Goal
Improve lifetime and I/O performance of modern SSDs by minimizing the negative impacts of erase operations
AERO (Adaptive ERase Operation)
Apply erase latency to be just long enough for reliably erasing a target flash block by accurately predicting the minimum erase latency of the flash block
Results
Improves lifetime by 43% and reduces read tail latency (P99.99) by 26%

## Slide 3: Outline
NAND Flash Basics
Erase Operation in Modern NAND Flash-Based SSDs
Adaptive Erase Operation (AERO)
  Fail-bit-count-based Erase Latency Prediction (FELP)
  Shallow Erasure
  Aggressive tEP Reduction
Evaluation Results

## Slide 4: NAND Flash Basics
NAND flash memory is hierarchically organized
Wordline0
WL1
Flash block
Flash cell
NAND string
BL0
BL1
BL2
Bitline3

## Slide 5: Program and Erase Operations
Program operation writes data in a WL granularity
WL0
WL1
Flash block
Flash cell
NAND string
BL0
BL1
BL2
BL3
Program (e.g., 20 V)
Program (e.g., 20 V)

## Slide 6: Program and Erase Operations
Erase operation erases data in a block granularity
WL0
WL1
Flash block
Flash cell
NAND string
BL0
BL1
BL2
BL3
Block erasure (e.g., 20 V)

## Slide 7: Program and Erase Operations
Erase operation erases data in a block granularity
Block erasure (e.g., 20 V)
Flash block
Flash cell
NAND string
BL0
BL1
BL2
BL3
Erase (program) operation only ejects (injects) electrons:
Erase-before-write property (data cannot be overwritten)

## Slide 8: Erase Operation: More Details
Erase operation consists of two steps
  Erase pulse (EP)
  Verify read (VR)
Voltage
Time
WL0
WL1
BL0
BL1
BL2
BL3

## Slide 9: Erase Operation: More Details
Erase operation consists of two steps
  Erase pulse (EP): Applies high voltage for fixed latency (3.5 )
  Verify read (VR)
Voltage
Time
WL0
WL1
BL0
BL1
BL2
BL3
ERASE 20 V
tEP = 3.5
(fixed)
ERASE

## Slide 10: Erase Operation: More Details
Erase operation consists of two steps
  Erase pulse (EP): Applies high voltage for fixed latency (3.5 )
  Verify read (VR): Checks if a block is completely erased
Voltage
Time
WL0
WL1
BL0
BL1
BL2
BL3
tEP = 3.5
(fixed)
ERASE
Completely erased
Finished!

## Slide 11: Erase Operation: More Details
Erase operation consists of two steps
  Erase pulse (EP): applies high voltage for fixed latency (3.5 )
  Verify read (VR): checks if a block is completely erased
Voltage
Time
WL0
WL1
BL0
BL1
BL2
BL3
tEP = 3.5
(fixed)
VERASE
Completely erased
Finished!
Long latency and high voltage in erase operations
Lifetime: A block becomes unusable after experiencing
a certain number of program and erase cycles (P/E cycles)

## Slide 12: Erase Operation: More Details
Erase operation consists of two steps
  Erase pulse (EP): applies high voltage for fixed latency (3.5 )
  Verify read (VR): checks if a block is completely erased
Voltage
Time
WL0
WL1
BL0
BL1
BL2
BL3
tEP = 3.5
(fixed)
VERASE
Completely erased
Finished!
Long latency and high voltage in erase operations
Lifetime: A block becomes unusable after experiencing
a certain number of program and erase cycles (P/E cycles)
Performance: An erase operation can delay user requests for a long time, significantly increasing read tail latency

## Slide 13: Erase Failure
As P/E cycle increases, it becomes difficult to erase a block
WL0
WL1
BL0
BL1
BL2
BL3
Voltage
tEP = 3.5
ERASE
Incompletely erased
Time

## Slide 14: Incremental Step Pulse Erasure (ISPE)
As P/E cycle increases, it becomes difficult to erase a block
  Performs additional erase pulse with higher voltage
WL0
WL1
BL0
BL1
BL2
BL3
Voltage
Time
tEP = 3.5
ERASE +
tEP = 3.5
ERASE +
Additional erase pulse
Finished!
Completely erased

## Slide 15: High Latency of Erase Operation
Erase failure frequently occurs as P/E cycle increases
Chart: P/E cycle count
| 0K | 1K | 2K | 3K | 4K | 5K
1 | 100 | 76.5 | 0 | 0 | 0 | 0
2 | 0 | 18.4 | 56.6 | 21.5 | 0 | 0
3 | 0 | 5.1 | 36.4 | 44.4 | 22.7 | 0
4 | 0 | 0 | 7 | 26.1 | 45.1 | 20.7
5 | 0 | 0 | 0 | 8 | 33.2 | 79.3
1 | 2 | 3 | 4 | 5
3.5 ms
7.0 ms
10.5 ms
14.0 ms
17.5 ms
# of EP steps:
Total erase latency (∑ tEP):

## Slide 16: High Latency of Erase Operation
Erase failure frequently occurs as P/E cycle increases
Chart: P/E cycle count
| 0K | 1K | 2K | 3K | 4K | 5K
1 | 100 | 76.5 | 0 | 0 | 0 | 0
2 | 0 | 18.4 | 56.6 | 21.5 | 0 | 0
3 | 0 | 5.1 | 36.4 | 44.4 | 22.7 | 0
4 | 0 | 0 | 7 | 26.1 | 45.1 | 20.7
5 | 0 | 0 | 0 | 8 | 33.2 | 79.3
1 | 2 | 3 | 4 | 5
3.5 ms
7.0 ms
10.5 ms
14.0 ms
17.5 ms
# of EP steps:
Total erase latency (∑ tEP):

## Slide 17: High Latency of Erase Operation
Chart: P/E cycle count
| 0K | 1K | 2K | 3K | 4K | 5K
1 | 100 | 76.5 | 0 | 0 | 0 | 0
2 | 0 | 18.4 | 56.6 | 21.5 | 0 | 0
3 | 0 | 5.1 | 36.4 | 44.4 | 22.7 | 0
4 | 0 | 0 | 7 | 26.1 | 45.1 | 20.7
5 | 0 | 0 | 0 | 8 | 33.2 | 79.3
Erase failure frequently occurs as P/E cycle increases
1 | 2 | 3 | 4 | 5
3.5 ms
7.0 ms
10.5 ms
14.0 ms
17.5 ms
# of EP steps:
Total erase latency (∑ tEP):
The negative impacts of erase operation become much higher as P/E cycle increases

## Slide 18: Erase Latency Variation
Actual erase latency significantly varies across flash blocks
Chart: P/E cycle count
| 0K | 1K | 2K | 3K | 4K | 5K
1 | 100 | 76.5 | 0 | 0 | 0 | 0
2 | 0 | 18.4 | 56.6 | 21.5 | 0 | 0
3 | 0 | 5.1 | 36.4 | 44.4 | 22.7 | 0
4 | 0 | 0 | 7 | 26.1 | 45.1 | 20.7
5 | 0 | 0 | 0 | 8 | 33.2 | 79.3
1 | 2 | 3 | 4 | 5
3.5 ms
7.0 ms
10.5 ms
14.0 ms
17.5 ms
# of EP steps:
Total erase latency (∑ tEP):

## Slide 19: Erase Latency Variation
Actual erase latency significantly varies across flash blocks
1 | 2 | 3 | 4 | 5
3.5 ms
7.0 ms
10.5 ms
14.0 ms
17.5 ms
# of EP steps:
Total erase latency (∑ tEP):
Chart: P/E cycle count
| 0K | 1K | 2K | 3K | 4K | 5K
1 | 100 | 76.5 | 0 | 0 | 0 | 0
2 | 0 | 18.4 | 56.6 | 21.5 | 0 | 0
3 | 0 | 5.1 | 36.4 | 44.4 | 22.7 | 0
4 | 0 | 0 | 7 | 26.1 | 45.1 | 20.7
5 | 0 | 0 | 0 | 8 | 33.2 | 79.3
45%

## Slide 20: Erase Latency Variation: Key Problem
Actual erase latency significantly varies across flash blocks
Chart: Total erase latency [ms]
| 8 | 8.5 | 9 | 9.5 | 10 | 10.5
17.77777778 | 17.7778 | 15.5556 | 14.4444 | 12.2222 | 11.1111 | 11.1111
Chart: P/E cycle count
| 0K | 1K | 2K | 3K | 4K | 5K
1 | 100 | 76.5 | 0 | 0 | 0 | 0
2 | 0 | 18.4 | 56.6 | 21.5 | 0 | 0
3 | 0 | 5.1 | 36.4 | 44.4 | 22.7 | 0
4 | 0 | 0 | 7 | 26.1 | 45.1 | 20.7
5 | 0 | 0 | 0 | 8 | 33.2 | 79.3
45%
1 | 2 | 3 | 4 | 5
3.5 ms
7.0 ms
10.5 ms
14.0 ms
17.5 ms
# of EP steps:
Total erase latency (∑ tEP):

## Slide 21: Erase Latency Variation: Key Problem
Actual erase latency significantly varies across flash blocks
Chart: Total erase latency [ms]
| 8 | 8.5 | 9 | 9.5 | 10 | 10.5
17.77777778 | 17.7778 | 15.5556 | 14.4444 | 12.2222 | 11.1111 | 11.1111
Chart: P/E cycle count
| 0K | 1K | 2K | 3K | 4K | 5K
1 | 100 | 76.5 | 0 | 0 | 0 | 0
2 | 0 | 18.4 | 56.6 | 21.5 | 0 | 0
3 | 0 | 5.1 | 36.4 | 44.4 | 22.7 | 0
4 | 0 | 0 | 7 | 26.1 | 45.1 | 20.7
5 | 0 | 0 | 0 | 8 | 33.2 | 79.3
45%
1 | 2 | 3 | 4 | 5
3.5 ms
7.0 ms
10.5 ms
14.0 ms
17.5 ms
# of EP steps:
Total erase latency (∑ tEP):

## Slide 22: Erase Latency Variation: Key Problem
Fixed latency of erase operation causes over-erase
Chart: Total erase latency [ms]
| 8 | 8.5 | 9 | 9.5 | 10 | 10.5
17.77777778 | 17.7778 | 15.5556 | 14.4444 | 12.2222 | 11.1111 | 11.1111
over-erased
89%
Chart: P/E cycle count
| 0K | 1K | 2K | 3K | 4K | 5K
1 | 100 | 76.5 | 0 | 0 | 0 | 0
2 | 0 | 18.4 | 56.6 | 21.5 | 0 | 0
3 | 0 | 5.1 | 36.4 | 44.4 | 22.7 | 0
4 | 0 | 0 | 7 | 26.1 | 45.1 | 20.7
5 | 0 | 0 | 0 | 8 | 33.2 | 79.3
45%
1 | 2 | 3 | 4 | 5
3.5 ms
7.0 ms
10.5 ms
14.0 ms
17.5 ms
# of EP steps:
Total erase latency (∑ tEP):

## Slide 23: Erase Latency Variation: Key Problem
1 | 2 | 3 | 4 | 5
3.5 ms
7.0 ms
14.0 ms
17.5 ms
# of EP steps:
Total erase latency (∑ tEP):
10.5 ms
89%
Chart: P/E cycle count
| 0K | 1K | 2K | 3K | 4K | 5K
1 | 100 | 76.5 | 0 | 0 | 0 | 0
2 | 0 | 18.4 | 56.6 | 21.5 | 0 | 0
3 | 0 | 5.1 | 36.4 | 44.4 | 22.7 | 0
4 | 0 | 0 | 7 | 26.1 | 45.1 | 20.7
5 | 0 | 0 | 0 | 8 | 33.2 | 79.3
Fixed latency of erase operation causes over-erase
Chart: Total erase latency [ms]
| 8 | 8.5 | 9 | 9.5 | 10 | 10.5
17.77777778 | 17.7778 | 15.5556 | 14.4444 | 12.2222 | 11.1111 | 11.1111
45%
over-erased
Key problem:
Fixed latency of erase operation causes unnecessary damages and delays

## Slide 24: Erase Latency Variation: Key Problem
Chart: P/E cycle count
| 0K | 1K | 2K | 3K | 4K | 5K
1 | 100 | 76.5 | 0 | 0 | 0 | 0
2 | 0 | 18.4 | 56.6 | 21.5 | 0 | 0
3 | 0 | 5.1 | 36.4 | 44.4 | 22.7 | 0
4 | 0 | 0 | 7 | 26.1 | 45.1 | 20.7
5 | 0 | 0 | 0 | 8 | 33.2 | 79.3
1 | 2 | 3 | 4 | 5
Fixed latency of erase operation causes over-erase
3.5 ms
7.0 ms
10.5 ms
14.0 ms
17.5 ms
Total fixed latency of erase pulses:
Chart: Total erase latency [ms]
| 8 | 8.5 | 9 | 9.5 | 10 | 10.5
17.77777778 | 17.7778 | 15.5556 | 14.4444 | 12.2222 | 11.1111 | 11.1111
45%
over-erased
# of erase pulses:
Key problem:
Fixed latency of erase operation causes unnecessary damages and delays
Goal:
Minimize erase latency to improve lifetime and I/O performance

## Slide 25: Outline
NAND Flash Basics
Erase Operation in Modern NAND Flash-Based SSDs
Adaptive Erase Operation (AERO)
  Fail-bit-count-based Erase Latency Prediction (FELP)
  Shallow Erasure
  Aggressive tEP Reduction
Evaluation Results

## Slide 26: Adaptive Erase Operation (AERO)
Voltage
Time
Fixed latency
WL0
BL0
BL1
BL2
BL3
Fixed latency can cause unnecessary damages and delays

## Slide 27: Adaptive Erase Operation (AERO)
Fixed latency can cause unnecessary damages and delays
Voltage
Time
Fixed latency
WL0
BL0
BL1
BL2
BL3
3.5
(fixed)
😵
😵
😵
😵
😵
😵
😵
😵
😵
😵

## Slide 28: Adaptive Erase Operation (AERO)
Fixed latency can cause unnecessary damages and delays
Voltage
Time
Fixed latency
Voltage
Time
Dynamic latency
3.5
(fixed)
WL0
BL0
BL1
BL2
BL3
WL0
BL0
BL1
BL2
BL3
😵
😵
😵
😵
😵
😵
😵
😵
😵
😵

## Slide 29: Adaptive Erase Operation (AERO)
Dynamic latency can minimize damages and delays
Voltage
Time
Fixed latency
Voltage
Time
Dynamic latency
3.5
(fixed)
WL0
BL0
BL1
BL2
BL3
😵
😵
😵
😵
😵
😵
😵
😵
😵
😵
WL0
BL0
BL1
BL2
BL3
😵
😵
1
(dynamic)
Reduced

## Slide 30: Adaptive Erase Operation (AERO)
Dynamic latency can minimize damages and delays
Voltage
Time
Fixed latency
Voltage
Time
Dynamic latency
3.5
(fixed)
WL0
BL0
BL1
BL2
BL3
😵
😵
😵
😵
😵
😵
😵
😵
😵
😵
WL0
BL0
BL1
BL2
BL3
😵
😵
1
(dynamic)
Reduced
Challenge: Erase latency varies across flash blocks even at the same P/E cycle  How to accurately predict erase latency?

## Slide 31: Fail-Bit-Count-Based ER. Latency Prediction
FELP predicts latency based on the fail-bit count
WL0
WL1
BL0
BL1
BL2
BL3
Voltage
tEP = 3.5
ERASE
Time

## Slide 32: Fail-Bit-Count-Based ER. Latency Prediction
BL1
BL3
FELP predicts latency based on the fail-bit count
  Verify read counts the number of un-erased bitlines (fail-bits)
WL0
WL1
BL0
BL1
BL2
BL3
Voltage
tEP = 3.5
ERASE
Fail-bit count = 2
Time

## Slide 33: Fail-Bit-Count-Based ER. Latency Prediction
FELP predicts latency based on the fail-bit count
  Verify read counts the number of un-erased bitlines (fail-bits)
  Initution: The lower the fail-bit count, the lower the latency
WL0
WL1
BL0
BL1
BL2
BL3
Voltage
tEP = 3.5
ERASE
Time
Fail-bit count = 2

## Slide 34: Fail-Bit-Count-Based ER. Latency Prediction
FELP predicts latency based on the fail-bit count
  Verify read counts the number of un-erased bitlines (fail-bits)
  Initution: The lower the fail-bit count, the lower the latency
WL0
WL1
BL0
BL1
BL2
BL3
Voltage
Time
Reduced!
ERASE +
tEP = 0.5 ~ 3.5
(dynamic)
Fail-bit count = 2

## Slide 35: Fail-Bit-Count-Based ER. Latency Prediction
FELP predicts latency based on the fail-bit count
  Verify read counts the number of un-erased bitlines (fail-bits)
  Initution: The lower the fail-bit count, the lower the latency
WL0
WL1
BL0
BL1
BL2
BL3
Voltage
Time
Reduced!
ERASE +
tEP = 0.5 ~ 3.5
(dynamic)
Fail-bit count = 2

## Slide 36: Observations for Optimization
Many blocks only require single erase pulse in early lifetime
Chart: P/E cycle count
| 0K | 1K | 2K | 3K | 4K | 5K
1 | 100 | 76.5 | 0 | 0 | 0 | 0
2 | 0 | 18.4 | 56.6 | 21.5 | 0 | 0
3 | 0 | 5.1 | 36.4 | 44.4 | 22.7 | 0
4 | 0 | 0 | 7 | 26.1 | 45.1 | 20.7
5 | 0 | 0 | 0 | 8 | 33.2 | 79.3
1 | 2 | 3 | 4 | 5
3.5 ms
7.0 ms
10.5 ms
14.0 ms
17.5 ms
# of EP steps:
Total erase latency (∑ tEP):

## Slide 37: Observations for Optimization
Many blocks only require single erase pulse in early lifetime
Chart: P/E cycle count
| 0K | 1K | 2K | 3K | 4K | 5K
1 | 100 | 76.5 | 0 | 0 | 0 | 0
2 | 0 | 18.4 | 56.6 | 21.5 | 0 | 0
3 | 0 | 5.1 | 36.4 | 44.4 | 22.7 | 0
4 | 0 | 0 | 7 | 26.1 | 45.1 | 20.7
5 | 0 | 0 | 0 | 8 | 33.2 | 79.3
1 | 2 | 3 | 4 | 5
3.5 ms
7.0 ms
10.5 ms
14.0 ms
17.5 ms
# of EP steps:
Total erase latency (∑ tEP):

## Slide 38: Optimization: Shallow Erasure
Split the first erase pulse into two parts
  Shallow erasure
  Remainder erasure
Voltage
Time
3.5
(fixed)

## Slide 39: Optimization: Shallow Erasure
Split the first erase pulse into two parts
  Shallow erasure: Short erasure with fixed latency (1 )
  Remainder erasure
Voltage
Time
3.5
(fixed)
1
Voltage
Time
1
(fixed)
Additional verify read

## Slide 40: Optimization: Shallow Erasure
Split the first erase pulse into two parts
  Shallow erasure: Short erasure with fixed latency (1 )
  Remainder erasure: Erasure based on FELP (0 ~ 2.5 )
1
Voltage
Time
1
(fixed)
2
0 ~ 2.5
(dynamic)
Voltage
Time
3.5
(fixed)
2
Reduced

## Slide 41: Optimization: Shallow Erasure
Split the first erase pulse into two parts
  Shallow erasure: Short erasure with fixed latency (1 )
  Remainder erasure: Erasure based on FELP (0 ~ 2.5 )
1
Voltage
Time
1
(fixed)
2
0 ~ 2.5
(dynamic)
Voltage
Time
3.5
(fixed)
2
Reduced
~80

## Slide 42: Optimization: Aggressive tEP Reduction
Allows incomplete erasure to further reduce erase latency
AERO w/o aggressive tEP reduction
Voltage
Time
WL0
BL0
BL1
BL2
BL3

## Slide 43: Optimization: Aggressive tEP Reduction
Allows incomplete erasure to further reduce erase latency
AERO w/o aggressive tEP reduction
Voltage
Time
WL0
BL0
BL1
BL2
BL3

## Slide 44: Optimization: Aggressive tEP Reduction
Allows incomplete erasure to further reduce erase latency
AERO w/o aggressive tEP reduction
AERO w/ aggressive tEP reduction
Voltage
Time
WL0
BL0
BL1
BL2
BL3
Voltage
Time
WL0
BL0
BL1
BL2
BL3

## Slide 45: Optimization: Aggressive tEP Reduction
Allows incomplete erasure to further reduce erase latency
  Inevitably causes more errors
AERO w/o aggressive tEP reduction
AERO w/ aggressive tEP reduction
Voltage
Time
WL0
BL0
BL1
BL2
BL3
Voltage
Time
WL0
BL0
BL1
BL2
BL3
Further reduced
Fail-bits

## Slide 46: Optimization: Aggressive tEP Reduction
Allows incomplete erasure to further reduce erase latency
  Inevitably causes more errors: Still can be corrected by ECC
AERO w/o aggressive tEP reduction
AERO w/ aggressive tEP reduction
Voltage
Time
WL0
BL0
BL1
BL2
BL3
Voltage
Time
WL0
BL0
BL1
BL2
BL3
Further reduced
Fail-bits
Corrected by ECC

## Slide 47: Feasibility Validation in the Paper
Using 160 real 3D TLC NAND flash chips, we study
Impact of erase pulse latency on the fail-bit count
Feasibility and parameter exploration of shallow erasure
Reliability characteristics of incompletely erased block
Applicability of AERO for other types of chips
  2D TLC
  3D MLC

## Slide 48: Implementation of AERO
Extend Flash translation layer (FTL) w/ two data structures

## Slide 49: Implementation of AERO
Extend Flash translation layer (FTL) w/ two data structures
  Shallow erasure flags (SEF): Check if shallow erasure is required
block ID | SEF
0 | T
 | T
… | …
- 1 | T
block ID | SEF
0 | T
 | T
… | …
 | T
Shallow erasure
flags (SEF)
FTL

## Slide 50: Implementation of AERO
Extend Flash translation layer (FTL) w/ two data structures
  Shallow erasure flags (SEF): Check if shallow erasure is required
  Erase-timing parameter table (EPT): Contains erase pulse latency
# | fail-bits | latency
0 | … | …
 |  | 2.5
1 |  | 0
 | … | …
… | … | …
# | fail-bits | latency
0 | … | …
1 |  | 
 | … | …
… | … | …
block ID | SEF
0 | T
 | T
… | …
- 1 | T
block ID | SEF
0 | T
 | T
… | …
 | T
Shallow erasure
flags (SEF)
Erase-timing parameter table (EPT)
FTL

## Slide 51: Implementation of AERO
Uses two existing commands to adjust erase latency
# | fail-bits | latency
0 | … | …
 |  | 2.5
1 |  | 0
 | … | …
… | … | …
# | fail-bits | latency
0 | … | …
1 |  | 
 | … | …
… | … | …
block ID | SEF
0 | T
 | T
… | …
- 1 | T
block ID | SEF
0 | T
 | T
… | …
 | T
Shallow erasure
flags (SEF)
Erase-timing parameter table (EPT)
FTL

## Slide 52: Implementation of AERO
Uses two existing commands to adjust erase latency
  GET FEATURE: Gets fail-bit counts from a flash chip
# | fail-bits | latency
0 | … | …
 |  | 2.5
1 |  | 0
 | … | …
… | … | …
# | fail-bits | latency
0 | … | …
1 |  | 
 | … | …
… | … | …
block ID | SEF
0 | T
 | T
… | …
- 1 | T
block ID | SEF
0 | T
 | T
… | …
 | T
Shallow erasure
flags (SEF)
Erase-timing parameter table (EPT)
FTL
Flash chip
GET FEATURE
Fail-bit counts

## Slide 53: Implementation of AERO
Uses two existing commands to adjust erase latency
  GET FEATURE: Gets fail-bit counts from a flash chip
  SET FEATURE: Sets latency of erase pulse
# | fail-bits | latency
0 | … | …
 |  | 2.5
1 |  | 0
 | … | …
… | … | …
# | fail-bits | latency
0 | … | …
1 |  | 
 | … | …
… | … | …
block ID | SEF
0 | T
 | T
… | …
- 1 | T
block ID | SEF
0 | T
 | T
… | …
 | T
Shallow erasure
flags (SEF)
Erase-timing parameter table (EPT)
FTL
Flash chip
SET FEATURE
Latency = 0.5

## Slide 54: Implementation of AERO
Step 1: Check the necessity of shallow erasure w/ SEF
  True: Performs shallow erasure for short latency (1 )
  False: Performs the first erase pulse for fixed latency (3.5 )
# | fail-bits | latency
0 | … | …
 |  | 2.5
1 |  | 0
 | … | …
… | … | …
# | fail-bits | latency
0 | … | …
1 |  | 
 | … | …
… | … | …
block ID | SEF
0 | T
 | T
… | …
- 1 | T
block ID | SEF
0 | T
 | T
… | …
 | T
Shallow erasure
flags (SEF)
Erase-timing parameter table (EPT)
FTL
Flash chip

## Slide 55: Implementation of AERO
Step 1: Check the necessity of shallow erasure w/ SEF
  True: Performs shallow erasure for short latency (1 )
  False: Performs the first erase pulse for fixed latency (3.5 )
# | fail-bits | latency
0 | … | …
 |  | 2.5
1 |  | 0
 | … | …
… | … | …
# | fail-bits | latency
0 | … | …
1 |  | 
 | … | …
… | … | …
block ID | SEF
0 | T
 | T
… | …
- 1 | T
block ID | SEF
0 | T
 | T
… | …
 | T
Shallow erasure
flags (SEF)
Erase-timing parameter table (EPT)
FTL
Flash chip
SET FEATURE
(1 ms)
Shallow erasure

## Slide 56: Implementation of AERO
Step 2: Queries the minimum erase-pulse latency by using
  The current number of erase pulse
  Fail-bit count
# | fail-bits | latency
0 | … | …
 |  | 2.5
1 |  | 0
 | … | …
… | … | …
# | fail-bits | latency
0 | … | …
1 |  | 
 | … | …
… | … | …
block ID | SEF
0 | T
 | T
… | …
- 1 | T
block ID | SEF
0 | T
 | T
… | …
 | T
Shallow erasure
flags (SEF)
Erase-timing parameter table (EPT)
FTL
Flash chip
Fail-bit count
GET FEATURE

## Slide 57: Implementation of AERO
Step 3: Sets the latency to perform the next erase pulse
# | fail-bits | latency
0 | … | …
 |  | 2.5
1 |  | 0
 | … | …
… | … | …
# | fail-bits | latency
0 | … | …
1 |  | 
 | … | …
… | … | …
block ID | SEF
0 | T
 | T
… | …
- 1 | T
block ID | SEF
0 | T
 | T
… | …
 | T
Shallow erasure
flags (SEF)
Erase-timing parameter table (EPT)
FTL
Flash chip
Erase
SET FEATURE
(2.5 ms)

## Slide 58: Implementation of AERO
Step 4: Modifies SEF to False if
  shallow erasure (1 ) + remainder erasure (2.5 ) 3.5
# | fail-bits | latency
0 | … | …
 |  | 2.5
1 |  | 0
 | … | …
… | … | …
# | fail-bits | latency
0 | … | …
1 |  | 
 | … | …
… | … | …
block ID | SEF
0 | T
 | T F
… | …
- 1 | T
block ID | SEF
0 | T
 | T F
… | …
 | T
Shallow erasure
flags (SEF)
Erase-timing parameter table (EPT)
FTL
Flash chip
Erase
SET FEATURE
(2.5 ms)

## Slide 59: Outline
NAND Flash Basics
Erase Operation in Modern NAND Flash-Based SSDs
Adaptive Erase Operation (AERO)
  Fail-bit-count-based Erase Latency Prediction (FELP)
  Shallow Erasure
  Aggressive tEP Reduction
Evaluation Results

## Slide 60: Evaluation
SSD Lifetime (metric: Maximum P/E Cycle Count)
Use 160 real 3D TLC NAND flash chips
I/O Performance (metric: Read Tail Latency)
Simulator: MQSim1 (extended with real-device characteristics)
Workload: 11 real-world I/O workloads
  5 from Alibaba traces
  6 from Microsoft Research Cambridge (MSRC) traces
Erase Schemes
Baseline:
AEROCONS: Dynamic erase pulse latency w/o aggressive tEP reduction
AERO
1Tavakkol et al., "MQSim: A Framework for Enabling Realistic Studies of Modern Multi-Queue SSD Devices," in FAST, 2018.
Dynamic erase pulse latency w/ aggressive tEP reduction
Conventional erase scheme (fixed erase pulse latency)

## Slide 61: Result: SSD Lifetime
Chart: 
| 0 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1,000 | 1,100 | 1,200 | 1,300 | 1,400 | 1,500 | 1,600 | 1,700 | 1,800 | 1,900 | 2,000 | 2,100 | 2,200 | 2,300 | 2,400 | 2,500 | 2,600 | 2,700 | 2,800 | 2,900 | 3,000 | 3,100 | 3,200 | 3,300 | 3,400 | 3,500 | 3,600 | 3,700 | 3,800 | 3,900 | 4,000 | 4,100 | 4,200 | 4,300 | 4,400 | 4,500 | 4,600 | 4,700 | 4,800 | 4,900 | 5,000 | 5,100 | 5,200 | 5,300 | 5,400 | 5,500 | 5,600 | 5,700 | 5,800 | 5,900 | 6,000 | 6,100 | 6,200 | 6,300 | 6,400 | 6,500 | 6,600 | 6,700 | 6,800 | 6,900 | 7,000 | 7,100 | 7,200 | 7,300 | 7,400 | 7,500 | 7,600 | 7,700 | 7,800 | 7,900 | 8,000
Baseline | 16 | 27 | 31 | 38 | 43 | 58 | 63
AEROCONS | 19 | 26 | 30 | 35 | 39 | 48 | 54.5 | 63
AERO | 46 | 48 | 53 | 53.5 | 52 | 57 | 55.5 | 60.5 | 63
0K | 1K | 2K | 3K | 4K | 5K | 6K | 7K | 8K
Avg. max. errors
P/E cycle count
Maximum correctable errors
Baseline
AEROCONS
AERO

## Slide 62: Result: SSD Lifetime
Chart: 
| 0 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1,000 | 1,100 | 1,200 | 1,300 | 1,400 | 1,500 | 1,600 | 1,700 | 1,800 | 1,900 | 2,000 | 2,100 | 2,200 | 2,300 | 2,400 | 2,500 | 2,600 | 2,700 | 2,800 | 2,900 | 3,000 | 3,100 | 3,200 | 3,300 | 3,400 | 3,500 | 3,600 | 3,700 | 3,800 | 3,900 | 4,000 | 4,100 | 4,200 | 4,300 | 4,400 | 4,500 | 4,600 | 4,700 | 4,800 | 4,900 | 5,000 | 5,100 | 5,200 | 5,300 | 5,400 | 5,500 | 5,600 | 5,700 | 5,800 | 5,900 | 6,000 | 6,100 | 6,200 | 6,300 | 6,400 | 6,500 | 6,600 | 6,700 | 6,800 | 6,900 | 7,000 | 7,100 | 7,200 | 7,300 | 7,400 | 7,500 | 7,600 | 7,700 | 7,800 | 7,900 | 8,000
Baseline | 16 | 27 | 31 | 38 | 43 | 58 | 63
AEROCONS | 19 | 26 | 30 | 35 | 39 | 48 | 54.5 | 63
AERO | 46 | 48 | 53 | 53.5 | 52 | 57 | 55.5 | 60.5 | 63
0K | 1K | 2K | 3K | 4K | 5K | 6K | 7K | 8K
Avg. max. errors
P/E cycle count
Maximum correctable errors
The end of lifetime
Baseline
AEROCONS
AERO

## Slide 63: Result: SSD Lifetime
Chart: 
| 0 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1,000 | 1,100 | 1,200 | 1,300 | 1,400 | 1,500 | 1,600 | 1,700 | 1,800 | 1,900 | 2,000 | 2,100 | 2,200 | 2,300 | 2,400 | 2,500 | 2,600 | 2,700 | 2,800 | 2,900 | 3,000 | 3,100 | 3,200 | 3,300 | 3,400 | 3,500 | 3,600 | 3,700 | 3,800 | 3,900 | 4,000 | 4,100 | 4,200 | 4,300 | 4,400 | 4,500 | 4,600 | 4,700 | 4,800 | 4,900 | 5,000 | 5,100 | 5,200 | 5,300 | 5,400 | 5,500 | 5,600 | 5,700 | 5,800 | 5,900 | 6,000 | 6,100 | 6,200 | 6,300 | 6,400 | 6,500 | 6,600 | 6,700 | 6,800 | 6,900 | 7,000 | 7,100 | 7,200 | 7,300 | 7,400 | 7,500 | 7,600 | 7,700 | 7,800 | 7,900 | 8,000
AERO | 46 | 48 | 53 | 53.5 | 52 | 57 | 55.5 | 60.5 | 63
Baseline | 16 | 27 | 31 | 38 | 43 | 58 | 63
AEROCONS | 19 | 26 | 30 | 35 | 39 | 48 | 54.5 | 63
0K | 1K | 2K | 3K | 4K | 5K | 6K | 7K | 8K
Avg. max. errors
P/E cycle count
Maximum correctable errors
Slowly increase
30%
Baseline
AEROCONS
AERO

## Slide 64: Result: SSD Lifetime
Chart: 
| 0 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1,000 | 1,100 | 1,200 | 1,300 | 1,400 | 1,500 | 1,600 | 1,700 | 1,800 | 1,900 | 2,000 | 2,100 | 2,200 | 2,300 | 2,400 | 2,500 | 2,600 | 2,700 | 2,800 | 2,900 | 3,000 | 3,100 | 3,200 | 3,300 | 3,400 | 3,500 | 3,600 | 3,700 | 3,800 | 3,900 | 4,000 | 4,100 | 4,200 | 4,300 | 4,400 | 4,500 | 4,600 | 4,700 | 4,800 | 4,900 | 5,000 | 5,100 | 5,200 | 5,300 | 5,400 | 5,500 | 5,600 | 5,700 | 5,800 | 5,900 | 6,000 | 6,100 | 6,200 | 6,300 | 6,400 | 6,500 | 6,600 | 6,700 | 6,800 | 6,900 | 7,000 | 7,100 | 7,200 | 7,300 | 7,400 | 7,500 | 7,600 | 7,700 | 7,800 | 7,900 | 8,000
Baseline | 16 | 27 | 31 | 38 | 43 | 58 | 63
AEROCONS | 19 | 26 | 30 | 35 | 39 | 48 | 54.5 | 63
AERO | 46 | 48 | 53 | 53.5 | 52 | 57 | 55.5 | 60.5 | 63
0K | 1K | 2K | 3K | 4K | 5K | 6K | 7K | 8K
Avg. max. errors
P/E cycle count
High errors due to incomplete erasure
Maximum correctable errors
Baseline
AEROCONS
AERO

## Slide 65: Result: SSD Lifetime
Chart: 
| 0 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1,000 | 1,100 | 1,200 | 1,300 | 1,400 | 1,500 | 1,600 | 1,700 | 1,800 | 1,900 | 2,000 | 2,100 | 2,200 | 2,300 | 2,400 | 2,500 | 2,600 | 2,700 | 2,800 | 2,900 | 3,000 | 3,100 | 3,200 | 3,300 | 3,400 | 3,500 | 3,600 | 3,700 | 3,800 | 3,900 | 4,000 | 4,100 | 4,200 | 4,300 | 4,400 | 4,500 | 4,600 | 4,700 | 4,800 | 4,900 | 5,000 | 5,100 | 5,200 | 5,300 | 5,400 | 5,500 | 5,600 | 5,700 | 5,800 | 5,900 | 6,000 | 6,100 | 6,200 | 6,300 | 6,400 | 6,500 | 6,600 | 6,700 | 6,800 | 6,900 | 7,000 | 7,100 | 7,200 | 7,300 | 7,400 | 7,500 | 7,600 | 7,700 | 7,800 | 7,900 | 8,000
Baseline | 16 | 27 | 31 | 38 | 43 | 58 | 63
AEROCONS | 19 | 26 | 30 | 35 | 39 | 48 | 54.5 | 63
AERO | 46 | 48 | 53 | 53.5 | 52 | 57 | 55.5 | 60.5 | 63
0K | 1K | 2K | 3K | 4K | 5K | 6K | 7K | 8K
Avg. max. errors
P/E cycle count
Slowly increase by minimzing erase latency
10%
Maximum correctable errors
Baseline
AEROCONS
AERO

## Slide 66: Result: SSD Lifetime
Chart: 
| 0 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1,000 | 1,100 | 1,200 | 1,300 | 1,400 | 1,500 | 1,600 | 1,700 | 1,800 | 1,900 | 2,000 | 2,100 | 2,200 | 2,300 | 2,400 | 2,500 | 2,600 | 2,700 | 2,800 | 2,900 | 3,000 | 3,100 | 3,200 | 3,300 | 3,400 | 3,500 | 3,600 | 3,700 | 3,800 | 3,900 | 4,000 | 4,100 | 4,200 | 4,300 | 4,400 | 4,500 | 4,600 | 4,700 | 4,800 | 4,900 | 5,000 | 5,100 | 5,200 | 5,300 | 5,400 | 5,500 | 5,600 | 5,700 | 5,800 | 5,900 | 6,000 | 6,100 | 6,200 | 6,300 | 6,400 | 6,500 | 6,600 | 6,700 | 6,800 | 6,900 | 7,000 | 7,100 | 7,200 | 7,300 | 7,400 | 7,500 | 7,600 | 7,700 | 7,800 | 7,900 | 8,000
Baseline | 16 | 27 | 31 | 38 | 43 | 58 | 63
AEROCONS | 19 | 26 | 30 | 35 | 39 | 48 | 54.5 | 63
AERO | 46 | 48 | 53 | 53.5 | 52 | 57 | 55.5 | 60.5 | 63
0K | 1K | 2K | 3K | 4K | 5K | 6K | 7K | 8K
Avg. max. errors
P/E cycle count
43%
Maximum correctable errors
Baseline
AEROCONS
AERO
10%
Slowly increase by minimzing erase latency

## Slide 67: Result: SSD Lifetime
Baseline
AEROCONS
AERO
Chart: 
| 0 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1,000 | 1,100 | 1,200 | 1,300 | 1,400 | 1,500 | 1,600 | 1,700 | 1,800 | 1,900 | 2,000 | 2,100 | 2,200 | 2,300 | 2,400 | 2,500 | 2,600 | 2,700 | 2,800 | 2,900 | 3,000 | 3,100 | 3,200 | 3,300 | 3,400 | 3,500 | 3,600 | 3,700 | 3,800 | 3,900 | 4,000 | 4,100 | 4,200 | 4,300 | 4,400 | 4,500 | 4,600 | 4,700 | 4,800 | 4,900 | 5,000 | 5,100 | 5,200 | 5,300 | 5,400 | 5,500 | 5,600 | 5,700 | 5,800 | 5,900 | 6,000 | 6,100 | 6,200 | 6,300 | 6,400 | 6,500 | 6,600 | 6,700 | 6,800 | 6,900 | 7,000 | 7,100 | 7,200 | 7,300 | 7,400 | 7,500 | 7,600 | 7,700 | 7,800 | 7,900 | 8,000
Baseline | 16 | 27 | 31 | 38 | 43 | 58 | 63
AEROCONS | 19 | 26 | 30 | 35 | 39 | 48 | 54.5 | 63
AERO | 46 | 48 | 53 | 53.5 | 52 | 57 | 55.5 | 60.5 | 63
0K | 1K | 2K | 3K | 4K | 5K | 6K | 7K | 8K
Avg. max. errors
P/E cycle count
43%
Maximum correctable errors
AERO significantly improves SSD lifetime

## Slide 68: Result: Read Tail Latency (P99.99, 0.5K PEC)
Chart: 
| ali.A | ali.B | ali.C | ali.D | ali.E | rsrch | stg | hm | prxy | proj | usr | G.M
Baseline | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
AERO1 | 0.77001 | 0.99922 | 0.6354 | 0.9991 | 0.99653 | 0.90132 | 0.99998 | 0.9515 | 0.30564 | 0.31396 | 0.97284 | 0.74453
AERO2 | 0.76214 | 0.99922 | 0.62096 | 0.99901 | 0.99623 | 0.90132 | 0.99998 | 0.9515 | 0.30311 | 0.30213 | 0.95949 | 0.73818
Normalized
read tail latency
ali.A | ali.B | ali.C | ali.D | ali.E | rsrch | stg | hm | prxy | proj | usr | G.M.
Baseline
AEROCONS
AERO

## Slide 69: Result: Read Tail Latency (P99.99, 0.5K PEC)
Chart: 
| ali.A | ali.B | ali.C | ali.D | ali.E | rsrch | stg | hm | prxy | proj | usr | G.M
Baseline | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
AERO1 | 0.77001 | 0.99922 | 0.6354 | 0.9991 | 0.99653 | 0.90132 | 0.99998 | 0.9515 | 0.30564 | 0.31396 | 0.97284 | 0.74453
AERO2 | 0.76214 | 0.99922 | 0.62096 | 0.99901 | 0.99623 | 0.90132 | 0.99998 | 0.9515 | 0.30311 | 0.30213 | 0.95949 | 0.73818
Normalized
read tail latency
26%
ali.A | ali.B | ali.C | ali.D | ali.E | rsrch | stg | hm | prxy | proj | usr | G.M.
Baseline
AEROCONS
AERO

## Slide 70: Result: Read Tail Latency (P99.99, 0.5K PEC)
Chart: 
| ali.A | ali.B | ali.C | ali.D | ali.E | rsrch | stg | hm | prxy | proj | usr | G.M
Baseline | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
AERO1 | 0.77001 | 0.99922 | 0.6354 | 0.9991 | 0.99653 | 0.90132 | 0.99998 | 0.9515 | 0.30564 | 0.31396 | 0.97284 | 0.74453
AERO2 | 0.76214 | 0.99922 | 0.62096 | 0.99901 | 0.99623 | 0.90132 | 0.99998 | 0.9515 | 0.30311 | 0.30213 | 0.95949 | 0.73818
Normalized
read tail latency
ali.A R: 7 W: 93 | ali.B | ali.C R: 69 W: 31 | ali.D | ali.E | rsrch R: 9 W: 91 | stg | hm | prxy R: 65 W: 35 | proj R: 88 W: 12 | usr | G.M.
Baseline
AEROCONS
AERO

## Slide 71: Result: Read Tail Latency (P99.99, 0.5K PEC)
Baseline
AEROCONS
AERO
Chart: 
| ali.A | ali.B | ali.C | ali.D | ali.E | rsrch | stg | hm | prxy | proj | usr | G.M
Baseline | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
AERO1 | 0.77001 | 0.99922 | 0.6354 | 0.9991 | 0.99653 | 0.90132 | 0.99998 | 0.9515 | 0.30564 | 0.31396 | 0.97284 | 0.74453
AERO2 | 0.76214 | 0.99922 | 0.62096 | 0.99901 | 0.99623 | 0.90132 | 0.99998 | 0.9515 | 0.30311 | 0.30213 | 0.95949 | 0.73818
Normalized
read tail latency
ali.A R: 7 W: 93 | ali.B | ali.C R: 69 W: 31 | ali.D | ali.E | rsrch R: 9 W: 91 | stg | hm | prxy R: 65 W: 35 | proj R: 88 W: 12 | usr | G.M.
Shallow erasure effectively reduces read tail latency in early lifetime
36

## Slide 72: Result: Read Tail Latency (P99.99, 2.5K PEC)
Chart: 
| ali.A | ali.B | ali.C | ali.D | ali.E | rsrch | stg | hm | prxy | proj | usr | G.M
Baseline | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
AERO1 | 0.68542 | 0.99877 | 0.70967 | 0.99812 | 0.99356 | 0.92315 | 0.97369 | 0.91249 | 0.7067 | 0.6396 | 0.82152 | 0.83991
AERO2 | 0.55898 | 0.99851 | 0.57011 | 0.99693 | 0.98985 | 0.90347 | 0.95181 | 0.89323 | 0.49723 | 0.41894 | 0.81071 | 0.74753
Normalized
read tail latency
ali.A | ali.B | ali.C | ali.D | ali.E | rsrch | stg | hm | prxy | proj | usr | G.M.
Baseline
AEROCONS
AERO

## Slide 73: Result: Read Tail Latency (P99.99, 2.5K PEC)
Chart: 
| ali.A | ali.B | ali.C | ali.D | ali.E | rsrch | stg | hm | prxy | proj | usr | G.M
Baseline | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
AERO1 | 0.68542 | 0.99877 | 0.70967 | 0.99812 | 0.99356 | 0.92315 | 0.97369 | 0.91249 | 0.7067 | 0.6396 | 0.82152 | 0.83991
AERO2 | 0.55898 | 0.99851 | 0.57011 | 0.99693 | 0.98985 | 0.90347 | 0.95181 | 0.89323 | 0.49723 | 0.41894 | 0.81071 | 0.74753
Normalized
read tail latency
ali.A R: 7 W: 93 | ali.B | ali.C R: 69 W: 31 | ali.D | ali.E | rsrch | stg | hm | prxy R: 65 W: 35 | proj R: 88 W: 12 | usr | G.M.
Baseline
AEROCONS
AERO

## Slide 74: Result: Read Tail Latency (P99.99, 2.5K PEC)
Baseline
AEROCONS
AERO
Chart: 
| ali.A | ali.B | ali.C | ali.D | ali.E | rsrch | stg | hm | prxy | proj | usr | G.M
Baseline | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
AERO1 | 0.68542 | 0.99877 | 0.70967 | 0.99812 | 0.99356 | 0.92315 | 0.97369 | 0.91249 | 0.7067 | 0.6396 | 0.82152 | 0.83991
AERO2 | 0.55898 | 0.99851 | 0.57011 | 0.99693 | 0.98985 | 0.90347 | 0.95181 | 0.89323 | 0.49723 | 0.41894 | 0.81071 | 0.74753
Normalized
read tail latency
ali.A R: 7 W: 93 | ali.B | ali.C R: 69 W: 31 | ali.D | ali.E | rsrch | stg | hm | prxy R: 65 W: 35 | proj R: 88 W: 12 | usr | G.M.
Aggressive tEP reduction further reduces read tail latency at higher P/E cycles (i.e., under high erase latency variation)

## Slide 75: Other Analyses in the Paper
Limitation of exisiting techniques
Implementation details
  Handling misprediction
  Impact of ECC-decoding latency
  Multi-plane operations
Evaluation
  Comparison with other exisiting techniques
  Impact of erase suspension
  Sensitivy analysis for misprediction rate and correctable errors
Please refer to the paper!

## Slide 76: Conclusion
Problem
Long and fixed latency of erase operation in modern SSDs degrade lifetime and I/O performance
AERO (Adaptive ERase Operation)
Fail-bit-count-based Erase Latency Prediction (FELP): dynamically adjusts erase latency
Shallow erasure: enables reducing latency of the first erase pulse
Aggressive tEP reduction: enables further reducing erase latency by exploiting the ECC capability
Results
Improves lifetime by 43% and reduces read tail latency (P99.99) by 26%

## Slide 77: AERO: Adaptive Erase Operation for Improving Lifetime and Performance of Modern NAND Flash-Based SSDs
Sungjun Cho1, Beomjun Kim2, Hyunuk Cho1, Gyeongseob Seo2,
Onur Mutlu3, Myungsuk Kim2, Jisung Park1
1
2
3
ASPLOS 2024
Session 9B: SSDs

## Slide 78: Cell States

## Slide 79: Validation: Fail-Bit Count vs Latency
Fail-bit count is highly correlated with the erase latency
Time
Voltage
Max fail-bit count [a.u.]
Erase pulse latency []
Chart: 
| 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5
R7 | 22258 | 17994 | 13541 | 9302 | 5144 | 1076 | 144
1: The number of erase loops = 3
2: 3.5
?
?

## Slide 80: Validation: Fail-Bit Count vs Latency
Fail-bit count is highly correlated with the erase latency
Max fail-bit count [a.u.]
Chart: 
| 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5
R7 | 22258 | 17994 | 13541 | 9302 | 5144 | 1076 | 144
Time
Voltage
0.5
?
Erase pulse latency []

## Slide 81: Validation: Fail-Bit Count vs Latency
Fail-bit count is highly correlated with the erase latency
Max fail-bit count [a.u.]
Time
Voltage
1
?
Chart: 
| 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5
R7 | 22258 | 17994 | 13541 | 9302 | 5144 | 1076 | 144
Erase pulse latency []

## Slide 82: Validation: Fail-Bit Count vs Latency
Fail-bit count is highly correlated with the erase latency
Max fail-bit count [a.u.]
Time
Voltage
3
?
Chart: 
| 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5
R7 | 22258 | 17994 | 13541 | 9302 | 5144 | 1076 | 144
0.5 ms
Erase pulse latency []

## Slide 83: Validation: Fail-Bit Count vs Latency
Fail-bit count is highly correlated with the erase latency
Max fail-bit count [a.u.]
Time
Voltage
3.5
?
Chart: 
| 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5
R7 | 22258 | 17994 | 13541 | 9302 | 5144 | 1076 | 144
Erase pulse latency []
0.5 ms

## Slide 84: Validation: Fail-Bit Count vs Latency
Fail-bit count is highly correlated with the erase latency
3.5 |  |  |  |  |  |  | 
3.0 |  |  |  |  |  |  | 
2.5 |  |  |  |  |  |  | 
2.0 |  |  |  |  |  |  | 
1.5 |  |  |  |  |  |  | 
1.0 |  |  |  |  |  |  | 
0.5 |  |  |  |  |  |  | 
# of erased blocks [%]
0
100
Erase pulse latency [ms]
Fail-bit count ranges
Time
Voltage
Fail-bit count = ?
?

## Slide 85: Validation: Fail-Bit Count vs Latency
Fail-bit count is highly correlated with the erase latency
3.5 |  |  |  |  |  |  | 
3.0 |  |  |  |  |  |  | 
2.5 |  |  |  |  |  |  | 
2.0 |  |  |  |  |  |  | 
1.5 |  |  |  |  |  |  | 
1.0 |  |  |  |  |  |  | 
0.5 |  |  |  |  |  |  | 
# of erased blocks [%]
0
100
Fail-bit count ranges
Time
Voltage
0 Fail-bit count
0.5 (100%)
Erase pulse latency [ms]

## Slide 86: Validation: Fail-Bit Count vs Latency
Fail-bit count is highly correlated with the erase latency
# of erased blocks [%]
0
100
Fail-bit count ranges
3.5 |  |  |  |  |  |  | 
3.0 |  |  |  |  |  |  | 
2.5 |  |  |  |  |  |  | 
2.0 |  |  |  |  |  |  | 
1.5 |  |  |  |  |  |  | 
1.0 |  |  |  |  |  |  | 
0.5 |  |  |  |  |  |  | 
Time
Voltage
Fail-bit count
1 (89%)
0.5 (11%)
11
89
Erase pulse latency [ms]

## Slide 87: Validation: Fail-Bit Count vs Latency
Fail-bit count is highly correlated with the erase latency
# of erased blocks [%]
0
100
Fail-bit count ranges
3.5 |  |  |  |  |  |  | 
3.0 |  |  |  |  |  |  | 
2.5 |  |  |  |  |  |  | 
2.0 |  |  |  |  |  |  | 
1.5 |  |  |  |  |  |  | 
1.0 |  |  |  |  |  |  | 
0.5 |  |  |  |  |  |  | 
Time
Voltage
Fail-bit count = ?
?
Erase pulse latency [ms]

## Slide 88: Validation: Fail-Bit Count vs Latency
Fail-bit count is highly correlated with the erase latency
# of erased blocks [%]
0
100
Fail-bit count ranges
3.5 |  |  |  |  |  |  | 
3.0 |  |  |  |  |  |  | 
2.5 |  |  |  |  |  |  | 
2.0 |  |  |  |  |  |  | 
1.5 |  |  |  |  |  |  | 
1.0 |  |  |  |  |  |  | 
0.5 |  |  |  |  |  |  | 
Time
Voltage
Fail-bit count = ?
?
Erase pulse latency [ms]

## Slide 89: Validation: Aggressive Reduction
Incompletely-erased blocks are stll safe to use
Time
Voltage
Chart: 
| F | 1 | A | 3 | B | 5 | 2B | 7 | 3B | 9 | 4B
0
Errors after prog. and read
Correctable errors
Fail-bit count in the second loop
 |  |  | 2 | 3 | 4
Skipped

## Slide 90: Validation: Aggressive Reduction
Incompletely-erased blocks are stll safe to use
Time
Voltage
Fail-bit count
Chart: 
| F | 1 | A | 3 | B | 5 | 2B | 7 | 3B | 9 | 4B
0
3 | #N/A | 42.3 | 50.25 | 58.2 | 65.75 | 73.3 | 81.35 | 89.4 | 97.1 | 104.8
Errors after prog. and read
 |  |  | 2 | 3 | 4
Correctable errors
Skipped
Fail-bit count in the second loop

## Slide 91: Validation: Aggressive Reduction
Incompletely-erased blocks are stll safe to use
Time
Voltage
Chart: 
| F | 1 | A | 3 | B | 5 | 2B | 7 | 3B | 9 | 4B
0
3 | #N/A | 42.3 | 50.25 | 58.2 | 65.75 | 73.3 | 81.35 | 89.4 | 97.1 | 104.8
Errors after prog. and read
 |  |  | 2 | 3 | 4
Correctable errors
Fail-bit count
Skipped
Fail-bit count in the second loop

## Slide 92: Validation: Aggressive Reduction
Incompletely-erased blocks are stll safe to use
Time
Voltage
Chart: 
| F | 1 | A | 3 | B | 5 | 2B | 7 | 3B | 9 | 4B
0
3 | #N/A | 42.3 | 50.25 | 58.2 | 65.75 | 73.3 | 81.35 | 89.4 | 97.1 | 104.8
Errors after prog. and read
 |  |  | 2 | 3 | 4
Correctable errors
0.5
(optimized)
Fail-bit count in the second loop
Fail-bit count

## Slide 93: Validation: Aggressive Reduction
Incompletely-erased blocks are stll safe to use
Time
Voltage
Chart: 
| F | 1 | A | 3 | B | 5 | 2B | 7 | 3B | 9 | 4B
0
3 | #N/A | 42.3 | 50.25 | 58.2 | 65.75 | 73.3 | 81.35 | 89.4 | 97.1 | 104.8
Errors after prog. and read
Correctable errors
0.5
(optimized)
Fail-bit count
Fail-bit count in the second loop
Fail-bit count
 |  |  | 2 | 3 | 4